## Slide 1: Task 1 Update
Peter Sharpe
Harvard-MIT Center for Advanced Climate Research

## Slide 2: Battery Modelling

## Slide 3: Battery Modelling: Where We Left Off
An energy stack-up is used to size Dawn’s battery.
We noticed strange results if the same stack-up was applied to Odysseus*:
* Assuming Odysseus is sized to 35N, Dec. 21; 265 Wh/kg @ cell
Possibilities:
Our physics models are wrong, and Dawn’s battery is oversized.
Odysseus’s battery is undersized.
The supplied Odysseus data is wrong.
Predicted w/ Dawn method
542 kg
As-built
275 kg
Odysseus Battery Mass
1.97x discrepancy! 
Using Odysseus information given to 16.82 class (outdated)

## Slide 4: Battery Modelling: Dawn Stack-up
Power Stack
Thrust power found by momentum argument
4.6 kW
Notes: Battery draw [4125] Motor terminals
Battery draw [289] Avionics
Battery draw [150] Payload (night)
Battery draw [46] Wiring losses
Motor terminals [3940] Propeller shaft power
Motor terminals [185] Motor losses
Propeller shaft power [3415] Thrust power (work)
Propeller shaft power [525] Propeller losses

## Slide 5: Battery Modelling: Dawn Stack-up
Energy Stack (Aug. 31, 49N)
4.6 kW
12 hr.
55.2 kWh
Night: 10.85 hr.
Night incl. twilight: 13.62 hr.
68.3 kWh
DoD
Notes: ' Type a list of Flows, like this:
' SOURCE [AMOUNT] TARGET
' Examples:
Usable energy [55.2] Ideal battery capacity
Battery discharge losses [1.4] Ideal battery capacity
Depth-of-Discharge losses [10] Ideal battery capacity
Ideal battery capacity [66.6] Battery capacity
Integer sizing losses [1.7] Battery capacity

## Slide 6: Battery Modelling: Dawn Stack-up
Mass Stack
68.3 kWh
Cell packing factor of 75%*:
BMS
Pack installation
Thermal management
* Slightly more optimistic than quotes from Ed Lovelace (70%).
202 kg
450 Wh/kg

## Slide 7: Battery Modelling: Resolved
Revised Odysseus numbers received from Kevin Uleck
Figure of Merit |  |  |  | Impact for Dawn sizing
Battery Specific Energy | 265 Wh/kg | → | 350 Wh/kg | N/A
Battery Depth of Discharge | 85% | → | 95% | Large, but is this realistic? Disagrees with electric aircraft lit. (~80-85%). Enabled by “SafeCell” tech?
Battery Packing Factor | 70% | → | 89% | Huge! Definitively true - Odysseus is an existence proof.
… |  | … |  | …
With new assumptions:
Predicted w/ Dawn method
287 kg
As-built
275 kg
Odysseus Battery Mass
1.04x discrepancy! 
Using Odysseus information given in personal correspondence (latest)

## Slide 8: Battery Modelling: Design Implications
Key assumptions (relative to CDR):
  Battery Depth of Discharge: 95%
  Battery Packing Factor: 89%
  MicroLink cells on mission airplane
Temporary; need to verify that this is realistic before baselining to this. Old value: 85%
To be used in all future analyses. Old value: 75%
Other assumptions:
  Aug. 31 night; wind N/A
  Battery Spec. Energy: 450 Wh/kg
  30 kg payload, 19.8 km (65.0 kft) min. altitude
  1.25x structural mass margin
  1.05x power generation margin
  Trajectory optimization allowed
  25.0% solar cell efficiency
  20% static margin
  180 W mean avionics power
  Many more…
suspect

## Slide 9: Battery Modelling: Design Implications
  Resulting airplane:
  33.1 m wingspan
  251 kg TOGW
  This is smaller than MIT Daedalus!!!

## Slide 10: Other Option: SunPower on Mission Airplane
  Resulting airplane:
  36.6 m wingspan
  265 kg TOGW
  Much cheaper + simpler development, but results in larger final airplane

## Slide 11: Trades

## Slide 12: Impacts of Battery Specific Energy
Our design

## Slide 13: Wingspan vs. TOGW: Pareto Plot

## Slide 14: Graphics for Pitches

## Slide 15: Graphics: Outer Mold Line

## Slide 16: Open Questions
Questions for Mark:
  Current secondary wing mass assumption:
    Daedalus-like component build up with 1.3x multiplier to reflect fragility of Daedalus
    Is 1.3x enough?
Questions for Task 2 team:
  Estimates for solar panel “glue weight” (if applicable and significant)?
    Actual glue
    Wiring between panels
  Restrictions on airfoil design (e.g. curvature) from solar panels?
Question for Tina:
  Do we have a Dropbox?